### Wi-Fi Standard and OSI Layer
Wi-Fi (Wireless Fidelity) follows the IEEE 802.11 standard, which defines wireless networking protocols for local area networks (WLANs). The Wi-Fi standard primarily operates at the Data Link Layer (Layer 2) and Physical Layer (Layer 1) of the OSI (Open Systems Interconnection) model.
### Breakdown of OSI Layers for Wi-Fi:
#### 1. Physical Layer (Layer 1)
- The Physical Layer (PHY) in Wi-Fi is responsible for the actual transmission of wireless signals over radio waves.
- It defines:
  - Frequency bands (2.4 GHz, 5 GHz, and 6 GHz)
  - Modulation techniques (e.g., OFDM, DSSS)
  - Data rates (e.g., Wi-Fi 4 = 600 Mbps, Wi-Fi 6 = 9.6 Gbps)
  - Transmission power
- Various Wi-Fi standards (802.11a/b/g/n/ac/ax) differ based on their PHY implementations.
#### 2. Data Link Layer (Layer 2)
- The Data Link Layer in Wi-Fi is divided into two sublayers:
  - Logical Link Control (LLC): Handles frame synchronization, error detection, and flow control.
  - Media Access Control (MAC): Controls how devices access the wireless medium (air), manages addressing, and handles authentication/encryption.
- The MAC sublayer in Wi-Fi defines:
  - CSMA/CA (Carrier Sense Multiple Access with Collision Avoidance) for network access
  - Frame formatting
  - Wireless security protocols (e.g., WPA2, WPA3)
  - Roaming between Access Points (APs)
### Why Not Higher Layers?
- Wi-Fi does not define network addressing (IP) or routing (Layer 3). Instead, higher-layer protocols like TCP/IP (Layer 3 & 4) operate on top of Wi-Fi.
- Application-layer services (Layer 7) such as web browsing, video streaming, and VoIP work over Wi-Fi but are not part of the Wi-Fi standard itself.
### Conclusion
- Wi-Fi operates at the Physical (Layer 1) and Data Link (Layer 2) layers of the OSI model.
- Physical Layer: Handles wireless signal transmission.
- Data Link Layer: Manages MAC addressing, security, and network access control.