### Difference Between IEEE 802.11a and IEEE 802.11b
IEEE 802.11a and IEEE 802.11b were both introduced in 1999, but they differ significantly in terms of frequency, speed, range, and adoption. Below is a comparison:
### 1. Comparison Table
Feature	IEEE 802.11a	IEEE 802.11b
Year Introduced	1999	1999
Frequency Band	5 GHz (UNII Band)	2.4 GHz (ISM Band)
Modulation Technique	OFDM (Orthogonal Frequency Division Multiplexing)	DSSS (Direct Sequence Spread Spectrum) with CCK
Maximum Data Rate	54 Mbps (Practical: ~20-25 Mbps)	11 Mbps (Practical: ~5-6 Mbps)
Other Supported Data Rates	6, 9, 12, 18, 24, 36, 48 Mbps	5.5, 2, and 1 Mbps (Adaptive Rate Selection)
Channel Bandwidth	20 MHz	22 MHz
Number of Subcarriers	52 (48 data, 4 pilot)	Not applicable
Carrier Separation	312.5 kHz	Not applicable
Symbol Duration	4 µsec (including 0.8 µsec guard interval)	Not applicable
Multipath Resistance	High (due to OFDM)	Low
Interference Level	Low (5 GHz is less crowded)	High (2.4 GHz is shared with Bluetooth, microwaves, etc.)
Range (Indoors)	Shorter (~35m)	Longer (~38m)
Compatibility	Not compatible with 802.11b	Compatible with later 802.11g
Adoption	Limited (due to high cost and short range)	Widely adopted (due to low cost and better range)